## Slide 1: JUNO - the Detector and Physics Plans
Jun Cao
Institute of High Energy Physics
INTERNATIONAL SCHOOL OF NUCLEAR PHYSICS, Erice-Sicily September 16-24, 2019

## Slide 2: The JUNO Experiment
20 kton LS detector
3% energy resolution
700 m underground
Rich physics possibilities
  Reactor neutrino for Mass Hierarchy and precision measurement of oscillation parameters
  Supernova neutrino
  Geo-neutrino
  Solar neutrino
  Atmospheric neutrino
  Proton decay
  Exotic searches
Talk by Y.F. Wang at ICFA seminar 2008, Neutel 2011; by J. Cao at Nutel 2009, NuTurn 2012;
Paper by L. Zhan, Y.F. Wang, J. Cao, L.J. Wen, PRD78:111103, 2008; PRD79:073007,2009
Jiangmen Underground Neutrino Observatory, a multiple-purpose neutrino experiment, approved in Feb. 2013, 300 M$

## Slide 3: Location of JUNO
Taishan NPP
Guang Zhou
Daya Bay
Hong Kong
JUNO
53 km
53 km
Yangjiang NPP
NPP | Daya Bay | Huizhou | Lufeng | Yangjiang | Taishan
Status | Operation | Planned | Planned | Operation | Operation / Pending
Power | 17.4 GW | 17.4 GW | 17.4 GW | 17.4 GW | 9.2 + 9.2 GW
700 m underground
20 kt Liquid scintillator
40 kt water shielding
JUNO-TAO
Shen Zhen

## Slide 4: JUNO Collaboration
77 institutions, 600 collaborators
China (34), Taiwan,China (3) Thailand (3), Pakistan, Armenia
Italy (8), Germany (7), France (5), Russia (3), Belgium, Czech, Finland, Latvia, Slovakia
Brazil (2), Chile (2), USA (3)

## Slide 5: Neutrino Mixing
2-neutrino oscillation: (Δm2, θ)
3-neutrino oscillation:
 6 oscillation parameters
Known: |Δm232| θ23 Δm221 θ12 θ13
Unknown: δCP Sign of Δm232

## Slide 6: Mass Hierarchy
Mass hierarchy: Which neutrino is the lightest?
Impacts on oscillation probability, MH and CP degeneracy.
Roadmap for 0 experiment
Understanding the mass origin and neutrino mixing in theory. Some GUT theories predict normal MH
Nucleosynthesis in supernova, neutrino mass scale … …

## Slide 7: MH with Reactor
and Interplay
and difference
Matter Effect
Atmospheric
Reactor
Accelerator
Petcov et al., PLB533(2002)94, J. Learned et al., PRD78, 071302 (2008), L. Zhan, Y. Wang, J. Cao, L. Wen, PRD78:111103, 2008, PRD79:073007, 2009
Relative measurement
Not rely on δCP and 23
JUNO energy resolution:

## Slide 8: Requirements for Reactor Experiment
Proper baseline: 45-60 km
Equal baselines
3% Energy resolution
100k events=20 kton35 GW6 year

## Slide 9: MH with Matter Effect
Accelerator, Atmospheirc
Both e appearance channel and  disappearance channel
Matter effect (aL) and CP asymmetry for neutrino and anti-neutrino due to electron in matter. Large effect at long distance
DUNE at 1300 km resolves degeneracy of MH and δCP
Appearance channel: Accelerator w/  and
NOvA, DUNE

## Slide 10: MH with absolute
T2K, NOvA
~ 1%
T2HK
~ 0.6% (10y)
JUNO | Statistics | +BG +1% b2b +1% EScale +1% EnonL
sin2 θ12 | 0.54% | 0.67%
Δm221 | 0.24% | 0.59%
Δm231 | 0.27% | 0.44%
NH:
IH:
~3%
NH
IH
DUNE

## Slide 11: JUNO Sensitivity for MH
3-4σ in 6y, 4-5σ in 10y
6 Years | Relative | w/ abs. Dm2
Statistics only | 4s | 5s
Realistic case | 3s | 4s

## Slide 12: MH with Supernova/Cosmology
Huiling Li, SNEWS, 2019
E. Worcester: Neutrino2018
Supernova burst
Pre-Supernova
Cosmology determine (m=m1+ m2+ m3) to 0.1 eV
|Dm232|~2.510-3 eV2
Dm221~710-5 eV2
K.N.Abazajian 2015 Astropart. Phys. 63 66

## Slide 13: Current Experiment – Super-K
5326 days, 328 kt.yr
Δχ2 = 4.34
CLs: Inverted MH rejection 80.6-96.7%
Normal MH
Inverted MH
Hayato, Neutrino2018

## Slide 14: Current Experiment - NOvA
Fermilab (700kW) to Minnesota (810 km). 14 kt LS detector
Prefer NH at 1.8σ
Extended running through 2024, proposed accelerator improvement
  3σ (if NH and δCP=3π/2) for allowed range of θ23 by 2020
  3σ for 30-50% (depending on octant) of δCP range by 2024.

## Slide 15: Large θ13 enables MH determination
3.4%
sin22θ13

## Slide 16: Next Generation Oscillation Exp
JUNO: 20 kton Liquid Scintillator
DUNE in US, 10-40 kton Liquid Argon
INO in India, 50 kton Iron+RPC
Hyper-K, T2HK in Japan, 260 kton water
PINGU at South Pole
ORCA in Mediterranean

## Slide 17: Mass Hierarchy
Just for demonstration. It depends on real schedule, real value of parameters, operation assumption, systematic assumption, etc.
P. Coyle
  NOvA: extended operation to 2025
  JUNO: 2021
  DUNE: 2026
  Hyper-K: 2027
  ORCA: 202x
  PINGU: 202x
  INO: Paused

## Slide 18: JUNO: Multiple Purpose Observatory
700 m
Sun
Cosmic Ray
100 k/day
After reducing 200,000 times w/ 700 m rock
Atmospheric ν
Several / day
Reactor ν
60 / day
Geo-ν
1 / day
Solar ν
10s - 1000s / day
JUNO, 20 kton LS
Supernova ν
5000 in 10s
@10kpc
26.6 GW, 53 km
JUNO Yellow book J. Phys. G 43, 030401 (2016)

## Slide 19: 2) Precision Measurements
 | Statistics | +BG +1% b2b +1% EScale +1% EnonL
sin2 θ12 | 0.54% | 0.67%
Δm221 | 0.24% | 0.59%
Δm231 | 0.27% | 0.44%
Probing the unitarity of UPMNS to 1%, New physics?
Current precision
Only JUNO can do!

## Slide 20: 3) Supernova Burst Neutrinos
Burst
Cooling
Accretion
Event Rate
SN@10kpc, w/ 1D simulations from Garching group
For particle physics:
Bound on absolute neutrino mass
Discriminate Mass ordering of neutrinos
Collective neutrino oscillation
…
For astrophysics:
SN explosion mechanism
Locating SN
Coincidence with Gravitational wave
SN nucleosynthesis
…

## Slide 21: 3) Supernova Burst Neutrinos
SN @ 10kpc
Full flavor detection and low threshold energy ~0.2MeV in LS (JUNO only)
IBD is the golden channel, ~5000 events for SN@10kpc
Especially the pES channel can provide us more information about , better than other type of detectors, e.g. WC, LAr-TPC detectors
PSD method to distinguish events from eES and pES

## Slide 22: 4) Diffused Supernova Neutrino Background
DSNB: Past core-collapse events
  10/sec in the visible universe
  Cosmic star-formation rate
  Core-collapse neutrino spectrum
  Rate of failed SNe
JUNO detection significance ~ 3
DSNB Observable window:
11 < < 30 MeV
3 events/year before PSD
10 Years’ sensitivity

## Slide 23: 5) Solar Neutrino
A new low-threshold (2MeV) 8B measurement (upturn + day/night asymmetry), solar and reactor discrepancy
1611.09867
solar metallicity problem
High Z
Low Z

## Slide 24: 6) Geo-neutrino
Geothermal energy: Earth’s interior thermodynamics.
Up to now, ~100 geo-ν observed by KamLAND and Borexino
400/year by JUNO
Discriminate BSE models

## Slide 25: 7) Proton Decay
Takaaki Kajita, Neutrino2018
Proton decay: physics at very high energy scale, where neutrino mass/mixing might be related with.
Hyper-K: ~1035 years for eπ0
JUNO: ~21034 years for νK+

## Slide 26: 8) Other
Atmospheric neutrino
  JUNO will have 1-2  sensitivity
    Measure both lepton and hadron energy
    Tracking and good energy resolution
Neutrinos from Dark Matter
  Annihilation in the Sun (Earth, Galaxy)
Exotic searches
  Non-standard interaction
  Lorentz invariance violation
  Sterile neutrino w/ reactor neutrino oscillation
  …

## Slide 27: Future: Double beta-decays
After MH measurement (~2030)
Cosmogenic backgrounds can be removed by a cut of LS volume along the muon track for seconds
  Active LS shielding is as effective as future dedicated 0ββ detectors
Zhao et al., arXiv: 1610.07143, CPC 41 (2017) 5
136Xe-loaded LS in balloon
130Te doped LS
1.35 /ton.yr

## Slide 28: JUNO Detector
LS | acrylic | water | PMT | Optical baffle | SS lattice | water | HDPE
17.7 m 0.12 1.43 0.8 0.5 1.2 m
JUNO CDR, arXiv_1508.07166

## Slide 29: State-of-Art LS Detector
Mass Hierarchy drives the detector specification
Unprecedented energy resolution (3%）
  PMT Coverage 78%
  PMT Detection Eff. > 27%
  LS attenuation length > 20 m
  Calibration
Low background (e.g. 1 ppt for acrylic, 10-15 g/g/ for LS)
20 times more statistics, mechanical challenges
Solar neutrino  low bkg 10-17 g/g for LS
Supernova neutrino  Electronics, Trigger, DAQ, Onsite computing
 Refresh many studies by an order
 | Daya Bay | BOREXINO | KamLAND | JUNO
Target Mass | ~20 t | ~300 t | ~1 kt | ~20 kt
Photoelectron Yield (PE/MeV) | ~160 | ~500 | ~250 | ~1200
Photocathode Coverage | ~12% | ~34% | ~34% | ~78%
Energy Resolution | ~8%/√E | ~5%/√E | ~6%/√E | 3%/√E

## Slide 30: Central Detector Design
March, 2014
July, 2015
SS truss+ Acrylic sphere
Balloon + Acrylic support+ SS tank
Acrylic sphere
+
SS truss
Balloon +
SS tank
Acrylic sphere +
SS tank
Acrylic module+
SS tank
Final decision:
Acrylic sphere + SS truss
SNO, SNO+
KamLAND, Borexino
Acrylic Sphere:
  ID: 35.4 m
  Thick:120 mm
SS truss:
  ID: 40.1 m
  OD: 41.1 m

## Slide 31: Central Detector Acrylic Sphere R&D
Panel size: 3m x 8m x 0.12m
Acrylic divided into 200+ panels
SS structure to hold a acrylic sphere and to mount PMTs
  Supporting bar to hold the Acrylic tank
  Stress of acrylic <3.5 MPa everywhere
Main issues:
  Mechanical precision for 3 mm PMT clearance
  Thermal expansion matching: 21oC  1oC
  Earth quake and liquid-solid coupling
  Transparency 96.5%, U/Th/K < 1 ppt
Started panel production

## Slide 32: Veto
Tasks:
  Shield rock-related backgrounds
  Tag & reconstruct cosmic-rays tracks
Detector:
  Top tracker: refurbished OPERA scintillators
  Water Č detector
Pool lining: HDPE
Earth magnetic field compensation coil

## Slide 33: Liquid Scintillator
System design & goal
  Long attenuation length: 15m>20m
    Al2O3 Filtration column
    Distillation
    Water extraction
    Gas stripping
  Highest possible light yield for JUNO：
    2.5 g/L PPO + 3 mg/L Bis-MSB
  Low radioactive backgrounds
    10-15 g/g for reactor
    10-17 g/g for solar neutrinos
OSIRIS
  An online detector with 20t LS for a sensitivity of 10-15 g/g per day
Linear Alky Benzene | Atte. L(m) @ 430 nm
RAW | 14.2
Vacuum distillation | 19.5
SiO2 coloum | 18.6
Al2O3 coloum | 22.3
LAB from Nanjing, Raw | 20
Al2O3 coloumn | 25
A pilot LS purification system at Daya Bay

## Slide 34: High QE PMT
A new type of PMT developed by IHEP & NNVC based on MCP to collect photoelectrons
  Intrinsically high collection efficiency
    No wire mesh in front of dynode
    transparent + reflective photocathode
  Easy for mass production
Performance
  MCP-PMT: good on DE, P/V, after pulse, bkg
  Dynode PMT: good on TTS,
Based on performance, cost, risk (DE>27%)
  MCP-PMT: 15000, first 8000, DE=28%*100%=28%, later >30%
  Dynode PMT: 5000, all delivered, DE =31%*90%= 28%
PDE | Mean（%）
All | 28.0
HAMAMATSU | 28.1
NNVT | 27.9

## Slide 35: Small PMT system
Calibrate non-uniformity and non-linearity of Large-PMTs
  Reduce energy scale uncertainty
  Improve energy resolution (non-stochastic term)
Increase optical coverage (~3%)
  Improve energy resolution (stochastic term)
Extend the energy measurement
  Improve muon physics
Independent system for Supernova
PMT Choice: 3” HZC XP72B22
Readout: Catiroc chip + GCU/HV/BEC for LPMT
  20” PMTs: 17631
  3” PMT: 25600

## Slide 36: PMT Instrumentation
PMT testing
  20,000 20” PMTs & 25,000 3” PMTs
  4 mass testing equip
PMT potting
  With base
  Failure rate < 0.5%/6 years
PMT protection
  Mechanism & requirements understood
  Acrylic + steel cover with holes
PMT installation

## Slide 37: Calibration
4 calibration facilities
  Routinely Source into LS by
    Automatic Calibration Unit: at central axis
    Rope Loop System : a plane
  Source into Guided Tube adhere to acrylic outer wall
  ROV: “sub-marine” anywhere in the LS
Choice of sources & location scan
  Simulation shows that the response map of the detector can be obtained
All has been prototyped and tested, proceeding for production

## Slide 38: Electronics
20000 ch. for LPMT & 100 m cable needed
Dynamic range: 1- 4000 PE
Noise: < 10% @ 1 PE
Resolution: 10%@1PE, 1%@100 PE
Failure rate: < 0.5%/6 years
Final solution: 1 GHz sampling FADC in a small box (3 ch. ) in water; all cables in corrugated pipes
芯片版图

## Slide 39: Software and Computing
  JUNO Software framework: SNiPER
  Unified detector description service for all applications
  Integrated the algorithms for physics generator, simulation, calibration, reconstruction and analysis
Geant4 based Simulation and reconstruction software
  Computing
  1/10 of final computing system was set, 1000 CPU cores and 1 PB disk storage
  Distributed computing platform was built based on DIRAC
Simulated 100 GeV Muon crossing JUNO
https://github.com/SNiPER-Framework/sniper

## Slide 40: Installation
SS Main Structure
Acrylic sphere
pool lining、Earth magnetic field shielding coils、Tyvek etc.
Acrylic sphere Installation platform
PMT Module
cover、Bridge、Cali.、TT in paralles
Clean
LS Filling
SS Main Structure
+Acrylic sphere
+PMT
+VETO+Cali.
In clean room, 21oC 1oC

## Slide 41: Civil Construction Status
1265 m @ slope of 42%
Vertical Tunnel: 563 m
Experimental hall
Overburden: 700 m
Width: 49 m
Length: 55 m
Surface building
A 50 m diameter, 70 m high cavern

## Slide 42: JUNO-TAO
Taishan Antineutrino Observatory (TAO), a ton-level, high energy resolution LS detector at 30m from the core, a satellite exp. of JUNO.
Measure reactor neutrino spectrum w/ sub-percent E resolution.
  Provide model-independent reference spectrum for JUNO
  Provide a benchmark for investigation of the nuclear database
Full coverage of SiPM with 50% PDE (-50 ℃) + LS  4500 p.e./MeV
  photon statistical resolution
  < 1% energy resolution for e+ at >3 MeV
Energy resolution
Ratio to Daya Bay 8% smearing
“True” spectrum by summation
3% (JUNO) smearing
TAO smearing
w/ statisitics (3y)

## Slide 43: JUNO-TAO Detector Concept
2.6 ton Gd-LS in a spherical vessel
  1-ton FV, 4000 ν’s/day
10 m2 SiPM of 50% PDE Operate at -50℃
From Inner to Outside
  Gd-LS working at -50℃
  SiPM and support
  Cryogenic vessel
  1~1.5 m water or HDPE shielding
  Muon veto
Laboratory in a basement at -10 m, 30-35 m from Taishan core (4.6 GW)
Plan to be online in 2021
Gd-LS
LAB

## Slide 44: JUNO-TAO Progress
Feasibility studies almost done
LS works at -50℃
Mechanical design in good shape
Readout options
Have a good understanding on budget
Measured onsite muon/neutron flux
Will prototype low temp. LS detector
Working on Conceptual Design Report

## Slide 45: Summary
JUNO is motivated to measure the Mass Hierarchy
  20 kton liquid scintillator
  3%/sqrt(E) energy resolution
  Advance detector technology
Rich physics program. World-leading studies on
  Precision measurement, Supernova ν, Geo-ν, solar ν, DSNB, proton decay, …
  Future JUNO-0νββ
Design, R&D, and most contracting done. Complete construction in 2021
New short-baseline experiment TAO, High energy solution measurement of reactor neutrino spectrum
  JUNO reference spectrum
  Benchmark for nuclear database

## Slide 46
UNESCO World Heritage

## Slide 47: Reactor Neutrino Detection
Delayed signal, Capture on H (2.2 MeV, 180s) or Gd (8 MeV, 30s)
Prompt signal
Capture on H
Capture on Gd
ν-e scattering
Inverse beta decay (IBD in LS)
0.1% Gd